## Slide 1: Regeltechniek WPO – Control engineering exercises
Dr. ir. Péter Zoltán CSURCSIA, PhD
peter.zoltan.csurcsia@vub.be

## Slide 2: WPO 5 sessies
Sessie | Beoordeling | Opmerking
WPO 1 inleiding, whiteboard oefeningen: polen en nullen, stabiliteit, Bodediagram, stapantwoord analyse, Simulink | Toets: 2 p | Een beoordeelde toets voor aanwezigheidscontrole.
WPO 2 Simulink oefeningen, gesloten lus controle, Ziegler-Nichols methoden. | Toets: 2p Werk: 3p | Een groep bevat max. 2 personen. Beoordeelde toets voor aanwezigheidscontrole. Studenten moeten een beoordeelde verslag schrijven.
WPO 3 labo oefening - PID-regeling 2 USB A poorten + Python | Toets: 2p Werk: 3p | 
WPO 4 PLC – labo oefening Ethernet (LAN)+ Windows | Toets: 1p Werk: 3p | 
WPO 5 PLC – labo oefening Ethernet (LAN)+ Windows | Toets: 1p Werk: 3p | Studenten moeten een beoordeelde verslag schrijven.
  WPO is 50% van de totaal.
  Overdragen punten naar 2de zit: indien meer dan 10 punten

## Slide 3: Rules
  Any kind of cheating results in 0 points
  No copy-paste, no sharing results, no reusing results,
  no discussion with other groups
  Three strikes during exercises
  You can ask always questions, if it is something what you should already know, then you have three strikes, after that -0.1p/question.
  You need to be able to explain and defend your results!
  You cannot explain your results => 0 point
  You wrongly explain your results and can correct => ½ points
  You can explain your miscalculated results and can correct =>full points
  No social media, no messaging, music (not loud) ok

## Slide 4: What will we learn?
Very basics only:
  Systems <> models
  Excitation signals
  Some of the most popular analysis techniques: Bode plot, step responses…
  Open and closed loop control
Tools
  Whiteboard v2.0
  Simulink toolbox (MATLAB)
  PLC, ball balancing lab exercises

## Slide 5: Test your Simulink installation
Step 2: create a blank model
Step 3: type ‘bode’ and ‘discrete impulse’ on the workspace. There should be blocks available with these names.
Step 1: type ‘simulink’ <enter>
1
2
3

## Slide 6: About myself
BEng in EE: Instumentation and measurement
BSc in technical informatics
Teacher’s diploma
MSc in embedded systems & applied informatics
PhD and Dr. ir. in (electrical) engineering
  Research area:
    Data-driven modeling (ML + SI)
    Nonlinear systems
    Vibration analysis
    Time-varying systems
    Signal processing

## Slide 7: Vibration analysis - nonlinearities
Problem 1: 100+ FRFs
Problem 2: users are not experts
Goal:
Tell the inexperienced users
1) if the system is linear
2) if it is safe to use a linear framework
3) gain in case of a nonlinear model

## Slide 8
Example: GVT of an airplane
eFusion Magnus aircraft

## Slide 9
Simroad testing

## Slide 10
Transient elimination

## Slide 11
Direct Field Acoustic eXcitation issues.
Nonlinearty assesment
Control
Example: DFAX

## Slide 12
http://sysidguy.eu/?page=msc&l=4
Master thesises

## Slide 13: Excitation signals
Unit pulse (impulse), u(s)=1
  The area of the impulse is one (A=1)
  Bad SNR
Unit step-signal (heavy-side function), u(s)=1/s
  Old-school, most-often used
  Height of the signal is 1 (A=1)
  Better SNR but high frequencies are not well excited
Unit ramp-signal, u(s)=1/s2
  Slope of the ramp signal is 1 (A=1)
Parabolic
Sine/cosine
Noise
…
SUT
u
y

## Slide 14: Test – unit pulse
  Sampling frequency (fs) is 1000 Hz.
SUT
u
y
  time [ms]
  1
  force [N]
  ?
  How much force should we apply for a unit pulse?
sysidguy.eu/vote
A | 0.001 [N]
B | 0.1 [N]
C | 1 [N]
D | 100 [N]
E | 1000 [N]

## Slide 15: SNR: Signal to Noise Ratio
  In reality,
  ideal signals (y) are measured with noise (n).
  ‘Goodness’ of the measurement is expressed by SNR.
SUT
u
y+n
  SNR in db =
  Average signal vs average noise
  mean=average
  Typical values in practice:
  Electrical measurement (e.g. audio filter) in labor: 60-90 dB
  Mechanical measurement (e.g. force) in vehicle testing: 40-60 dB
  Industrial temperature in ovens: 20-30 dB.
0 dB (1:1, 100%)
20 dB (1:10, 10%)
40 dB (1:100, 1%)
60 dB (1:1000, 0.1%)
80 dB (1:10000)

## Slide 16: Test – unit pulse
  Sampling frequency (fs) is 1000 Hz.
  Measurement is 1 second long.
  Unit pulse is applied.
  Noise on the measurement ±1 N.
SUT
u
y
A | 0 dB (1:1)
B | 20 dB (1:10)
C | 40 dB (1:100)
D | 60 dB (1:1000)
E | 80 dB (1:10000)
  How much is the SNR (Signal to Noise Ratio)?
sysidguy.eu/vote

## Slide 17: Models in general
Time domain
Fourier
Frequency domain
𝑠=𝑗𝜔
Laplace domain
Laplace
Differential/ Difference equation
State-space equations
Impulse response (measurements)
Step response (measurements)
Ramp response (measurement)
Etc…
Frequency Response Function
Bode plot
Nyquist plot
Etc…
Differential/ Difference equation
  ,
Pole-zero plots
Etc…

## Slide 18
Impulse response
Step response
Bode plot
Differential equations
  Transfer function form
  Zero Pole Gain form
Pole-zero plots
Time domain
Fourier
Frequency domain
𝑆=𝑗𝜔
Laplace domain
Laplace
Models in the WPO session

## Slide 19: ZP map - stability
https://jyotsnaj.wordpress.com/2009/10/01/question-3-what-do-the-poles-and-zeros-contribute-to-in-the-control-system/
marginally stable (not stable!)
Poles (denoted by x) should be on the left side of the S-plane
Zeros (denoted by o) changes the shape of the response.

## Slide 20: Poles in ZP map
Time scale of the decay
https://www.dummies.com/education/science/science-electronics/s-domain-analysis-understanding-poles-and-zeros-of-fs/
frequency scale of the oscillation
Combination

## Slide 21: Differential equation example 1a
SUT
u
y
  Questions:
  How do you convert this to s domain?
  What is the transfer function? Order of the system?
  What are the poles and zeros? Stability? ZP map? Simplification
  Natural frequency, time constant, damping factor?
  Time domain plot: impulse and step responses
  Steady-state error (open loop) for impulse and step response
  What is the ZPK (zero pole gain) format? Bode diagram?

## Slide 22: Differential equation example 1a
apply Laplace transformation
S domain form
Transfer function form
SUT
u
y

## Slide 23: Differential equation example 1a
S domain form
Transfer function form
Second order system
Zeros and poles:
SUT
u
y

## Slide 24: Differential equation example 1a
S domain form
Transfer function form
Second order system
Zeros and poles: zeros: -3 ; poles=-2 / -3;
can be rewritten as
  First order system: pole-zero cancellation
  The system’s model is 2nd order but when observed we will see 1st order only.
  Time constant=-1/real(pole)=0.5 Damping factor= -real(pole)/abs(pole)=1
  Natural frequency=abs(pole)=2 [rad/s]
SUT
u
y

## Slide 25: Differential equation example 1a
Transfer function form
Time domain plots of the impulse response function?
SUT
u
y

## Slide 26: Differential equation example 1a
Transfer function form
Time domain plots of the impulse response function?
SUT
u
y
)=1

## Slide 27: Differential equation example 1a
Transfer function form
Time domain plots of the impulse response function?
SUT
u
y
)=1
)=0

## Slide 28: Differential equation example 1a
Transfer function form
Time domain plots of the impulse response function?
SUT
u
y
)=1
)=0
=-1/real(pole)=0.5 sec

## Slide 29: Differential equation example 1a
Transfer function form
Time domain plots of the step response function?
SUT
u
y
=-1/real(pole)=0.5 sec
  at this time is the step response

## Slide 30: Differential equation example 1a
Transfer function form
Time domain plots of the step response function?
SUT
u
y
=-1/real(pole)=0.5 sec
  at this time is the step response
  Simulation/measurement time should be at least 10-times larger than the dominant time constant.
  = static gain = H(s=0)

## Slide 31: Differential equation example 1a
Transfer function form
What is the zero pole gain format (zpk)?
SUT
u
y

## Slide 32: Differential equation example 1a
Transfer function form
What is the zero pole gain format (zpk)?
  zeros: -3 ; poles=-2 / -3;
  static gain:
  Static gain is always same in all representation
  =?
SUT
u
y

## Slide 33: Differential equation example 1a
Transfer function form
What is the zero pole gain format (zpk)?
  zeros: -3 ; poles=-2 / -3;
  static gain:
  Static gain is always same in all representation
  =1
SUT
u
y

## Slide 34: Some Laplace transform pairs

## Slide 35: Example 2
  Transfer function
  Questions:
  What are the poles and zeros? Stability? ZP map? Simplification?
  Time domain plot: impulse and step responses (static gain!)

## Slide 36: Example 2
  Solutions:
  Zero 1:
  Zero 2:
  Pole 1,2:
  Dead-time: 5 sec
  Impulse response:
  Initial value:
  Final value:
  Time constant: ?
  Oscillation frequency: ?
  Damping factor: ?

## Slide 37: Example 2
  Solutions:
  Zero 1:
  Zero 2:
  Pole 1,2:
  Dead-time: 5 sec
  Impulse response:
  Initial value:
  Final value:
  Time constant: 0.5 sec
  Oscillation frequency: 2,24 rad/sec Damping factor= 0,89
  Step response:
  Initial value:
  Static gain:

## Slide 38: Example 2
  Solutions:
  Zero 1:
  Zero 2:
  Pole 1,2:
  Dead-time: 5 sec
  Impulse response:
  Initial value:
  Finial value:
  Time constant: 0.5 sec
  Oscillation frequency: 2,24 rad/sec Damping factor= 0,89
  Step response:
  Initial value:
  Static gain:

## Slide 39: Connecting blocks - book
Serial connection (cascading)
  Products of the elements
Parallel connection
  Sum of the elements
Feedback

## Slide 40: Connecting blocks
X(s)
-
Y(s)
X(s)
Y(s)
X(s)
-
Y(s)
-
Y(s)
X(s)
-
Y(s)
X(s)
-
X(s)
Y(s)
Moving entry point backwards
Moving the exit point forwards
  Divide with the element moved over
Moving the entry point forwards
Moving the exit point backwards
  Multiple with the element moved over

## Slide 41: Simplification example

## Slide 42: Simplification example
1+D

## Slide 43: Simplification example
1+D+I

## Slide 44: Simplification example
KH(1+D+I)

## Slide 45: Simplification example

## Slide 46: Simplification example
loop gain (function)
Characteristic polynomial

## Slide 47: Simplification example - advanced
Solution is given
http://sysidguy.eu/regeltechniek/plant_simplify.pdf

## Slide 48: Example
u(t)=4*h(t)
-
  Steady-state values:
  Reference signal (R)?
  Process value (PV)?
  Static error?
  Measured process value (MPV)?
  Error signal?

## Slide 49: Example
u(t)=4*h(t)
-
  Steady-state values:
  Reference signal (R)? 4*5=20
  Process value (PV)? 20*(1/2)/(1+(1/2)(8/4))=5
  Static error? 4-5=-1
  Measured process value (MPV)? PV*(8/4)=10
  Error signal? R-MPV=10
  20
  5
  10
  10

## Slide 50: Step response 1
Static gain= when unity step response, 0 starting value
Overshoot (undershoot: min(y))

## Slide 51: Step response 2

## Slide 52: Unit step response – example
  Order of the system: ?
  Static gain: ?
  Settling time: ?
  Rise time: ?
  Overshoot: ?
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 53: Unit step response – example
  Order of the system: 1 (probably)
  Static gain: 0.5
  Settling time: ?
  Rise time: ?
  Overshoot: ?
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 54: Unit step response – example
  Order of the system: 1 (probably)
  Static gain: 0.5
  Settling time: 1.9 sec
  Rise time: around 1.2 sec (1.3-0.1)
  Overshoot: ?
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 55: Unit step response – example
  Order of the system: 1 (probably)
  Static gain: 0.5
  Settling time: 1.9 sec
  Rise time: around 1.2 sec (1.3-0.1)
  Overshoot: 0 % ([0.5-0.5]/0.5*100)
  Dead time: 0
  Time constant: around 0.5 sec (amplitude is near 0.5*63%=0,315)
  Steady-state error: 0.5

## Slide 56: Step response – example 2
  Order of the system: ?
  Static gain: ?
  Settling time: ?
  Rise time: ?
  Overshoot: ?
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 57: Step response – example 2
  Order of the system: probably 2
  Static gain: 2 [=(6-2)/(3-1)]
  Settling time: ?
  Rise time: ?
  Overshoot: ?
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 58: Step response – example 2
  Order of the system: probably 2
  Static gain: 2 [=(6-2)/(3-1)]
  Settling time: around 7.2 sec
  Rise time: around 0.28 sec (5.3-5.02)
  Overshoot: 20% [(7.2-6)/6*100]
  Dead time: ?
  Time constant: ?
  Steady-state error: ?

## Slide 59: Step response – example 2
  Order of the system: probably 2
  Static gain: 2 [=(6-2)/(3-1)]
  Settling time: around 7.2 sec
  Rise time: around 0.28 sec (5.3-5.02)
  Overshoot: 20% [(7.2-6)/6*100]
  Dead time: 5 sec
  Time constant: 0.2 sec (=5.2-5 [dead time!], 63% of the jump 4=> 2.5]
  Steady-state error: 3 (6-3)

## Slide 60: Bode plot - application

## Slide 61: Bode plot - application

## Slide 62: Bode plot - application
17.44 Hz
33.175 Hz
63.688 Hz
75.957 Hz
87.184 Hz
91.502 Hz

## Slide 63: Test – Bode diagram
Consider the closed loop system with the following components.
A | Controller*System
B | Controller*System*Sensor
C | System
D | Controller*System/ (1+Controller*System*Sensor)
What elements are used to plot the Bode function?

## Slide 64: Measurement of Bode diagram
Consider the manual measurement of the Bode plot.
A | Pulse
B | Square
C | Ramp
D | Sine
E | none of the above
Which signal would you apply?
SUT

## Slide 65: Bode plot – units
Magnitude
Phase P [deg or rad]
SUT
u
y

## Slide 66: Bode plot – frequency scale
Rad/sec or Hz (other units are also possible)
Normalized of absolute
Decade (log10), octave (log8), linear, etc.

## Slide 67: Bode plot – useful derivations
Advantage of logarithmic scale:
Magnitude to dB:
dB to Magnitude:
Phase: 180 deg = 1 Pi
Frequency omega [rad]=>2*pi*F [Hz]

## Slide 68: Bode plot – useful derivations
Idea of behind stability - Closed loop equation
characteristic polynomial
Unstable if F(s)G(s)=-1 db(|1|)=0
-1 =>-180 deg
Loop gain (function)
F(s)G(s)
http://sysidguy.eu/regeltechniek/bode_by_hand.pptx
Manual drawing examples

## Slide 69: Bode plot overview - quantities
Static gain = DC gain: magnitude of H(s→0)=>H(jω→0)

## Slide 70: Bode plot overview - quantities
Time constants – frequencies - Poles/Zeros:
Check the frequencies at ±3 dB*n at the breaking point (bandwidth) n order of the system
-3 dB
-3 dB
Middle point of phase change

## Slide 71: Bode plot overview - quantities
Time constants – frequencies - Poles/Zeros:
Check the frequencies at ±3 dB at the breaking point (bandwidth)
A | fL
B | fU
C | 2*fL
D | 2*fU
E | 2*B
  Minimum sampling frequency?

## Slide 72: Bode plot overview - quantities
(gain) cross-over frequency: where the magnitude crosses 0 dB
Phase margin: 180 deg – phase at cross-over
cross-over frequency
phase
margin

## Slide 73: Bode plot overview - quantities
phase cross-over frequency: where the phase crosses 180 deg
gain margin: -(magnitude at phase cross-over)
phase cross-over frequency
gain
margin

## Slide 74: Bode plot overview - stability
In practice, stable if PM>45 deg and gm>0

## Slide 75: P - Proportional term – 0 order tf

## Slide 76: I - Integral term
20 dB/D

## Slide 77: PI – Proportional Integral term
20 dB/D

## Slide 78: D – Derivative term
20 dB/D

## Slide 79: Dead time/ delay term

## Slide 80: T1 – 1st order term
20 dB/D
45 deg/D

## Slide 81: T1 – 1st order term
20 dB/D
45 deg/D

## Slide 82: PT1 – Proportional 1st order term
20 dB/D
45 deg/D

## Slide 83: T2 – 2nd order term as 2 T1 terms
20 dB/D
45 deg/D
40 dB/D
90 deg/D
45 deg/D

## Slide 84: T2 – 2nd order term, zeta=1
40 dB/D
90 deg/D

## Slide 85: T2 – 2nd order term, zeta=0.1

## Slide 86: T2 – 2nd order term, zeta=0.01

## Slide 87: Bode example 1
Order of system=?
Type of system=?
Static gain=?
Pole frequency=?
Cross-over fr.=?
Phase margin=?
Gain margin=?
Stable=?

## Slide 88: Bode example 2
Order of system=?
Type of system=?
Static gain=?
Pole frequency=?
Cross-over fr.=?
Phase margin=?
Gain margin=?
Stable=?

## Slide 89
Simulink exercises

## Slide 90: Exercise
Some various materials from previous year: http://sysidguy.eu/index.php?page=teaching2021&l=4
Typical mistakes
  Simulation time is too short and/or wrong scaling

## Slide 91: Bode diagram block
Make sure you use open-loop signals
Use exact delay should be ticked (otherwise your dead-time is not shown correctly)

## Slide 92: Solver options
The sampling frequency (sampling time) can be set by modifying the solver parameters (fixed step size, see the icon on the bottom right corner of the Simulink window).

## Slide 93: System with fs=100 Hz
Realize the system in Simulink.
Calculate the zeros and poles yourself. Plot the poles and zeros in Simulink and compare with your results. What is the dominant time constant?
Simulate a unit step response excitation. Choose an appropriate time interval for the simulation (based on the time constant). The sampling frequency (sampling time) can be set by modifying the solver parameters (fixed step size).
Plot the step response. Quantify the step response: static gain, rise time, settling time, peak-time, dominant time constant.
Show clearly on your plot how you estimate the different quantities
Display the Bode plot. Analyze: static gain, time constants (which one is the dominant one), gain margin, phase margin, cross-over frequency.
How do you obtain the step response if only the impulse response is available? Simulate the impulse response (hint: use discrete impulse block). Compare the step response and the step response estimate from the impulse response, show that they are equal.

## Slide 94: Closed loop control
a) Realize the systems with the following parameters
Is the open-loop system stable? Show the unit step response.
Is the closed-loop system stable? Show the unit step response.
b) Display the Bode plot of the underlying system.
Estimate the gain margin, phase margin, crossover frequency using the Bode plot figure.
c) Design a closed loop P controller. What gain is needed? Why? Define the controller accordingly.