## Slide 1: Regeltechniek WPO – Control engineering exercises
Dr. ir. Péter Zoltán Csurcsia

## Slide 2: In case of problems
In case of problems: peter.zoltan.csurcsia@vub.be
Website:
http://homepages.vub.ac.be/~pcsurcsi
For appointments: agenda online available

## Slide 3: Why no ‘real’ lab exercises?

## Slide 4: What will be instead?
Theoretical analysis and
mathematical derivation

## Slide 5: What will we learn?
Very basics only:
  Systems <> models
  Excitation signals
  Some of the most popular analysis techniques: Bode plot, step responses…
  Open and closed loop control
Tools
  Whiteboard v0.0
  Control engineering toolbox (MATLAB)
  Simulink toolbox (MATLAB)

## Slide 6: Matlab vs Phython
Control systems
Control systems

## Slide 7: About the exercises: 4 sessions
1) Starting up: Matlab-control engineering toolbox
  Report writing, can work in a group of 2-3
2) Control engineering toolbox
  Paper based test for 5 points
  Report writing to regeltechniekwpo@gmail.com, can work in a group of 2-3
3) More theoretical-control engineering toolbox
  Paper based test for 5 points
  Report writing to regeltechniekwpo@gmail.com, can work in a group of 2-3
4) Simulink toolbox
  Paper based test for 5 points
  Pratical test to be organized
  Simulink test for 5 points
  WPO is 30% of the total. You can carry your points if you have min. 10.

## Slide 8: About myself
BEng in EE: Instumentation and measurement
BSc in technical informatics
Teacher’s diploma
MSc in embedded systems & applied informatics
PhD and Dr. ir. in (electrical) engineering
  Research area:
    Nonlinear systems
    Vibration analysis
    Time-varying systems
    Signal processing

## Slide 9: Vibarion analysis - nonlinearities
Problem 1: 100+ FRFs
Problem 2: users are not experts
Goal:
Tell the unexperienced users
1) if the system is linear
2) if it is safe to use a linear framework
3) gain in case of a nonlinear model

## Slide 10
Example: GVT of an airplane
eFusion Magnus aircraft

## Slide 11
Transient elimination

## Slide 12
Direct Field Acoustic eXcitation issues.
Nonlinearty assesment
Control
Example: DFAX

## Slide 13: Excitation signals
Unit impulse
  The area of the impulse is one (A=1)
  Bad SNR
Unit step-signal (heavy-side function)
  Old-school most-often used
  Height of the signal is 1 (A=1)
  Better SNR but high frequencies are not well excited
Unit ramp-signal
  Slope of the ramp signal is 1 (A=1)
Parabolic
Sine/cosine
Noise
…
SUT
u
y

## Slide 14: Models in general
Time domain
Fourier
Frequency domain
𝑠=𝑗𝜔
Laplace domain
Laplace
Differential/ Difference equation
State-space equations
Impulse response (measurements)
Step response (measurements)
Ramp response (measurement)
Etc…
Frequency Response Function
Bode plot
Nyquist plot
Etc…
Differential/ Difference equation
  ,
Pole-zero plots
Etc…

## Slide 15
Impulse response
Step response
Bode plot
Differential equations
  Transfer function form
  Zero Pole Gain form
Pole-zero plots
Time domain
Fourier
Frequency domain
𝑆=𝑗𝜔
Laplace domain
Laplace
Models in the WPO session

## Slide 16: Differential equation example
=> Laplace transformation
  Transfer function form =>
  zeros: -3 ; poles=-2 / -3; static gain:
  Zero Pole Gain form =>
  when K=1 the 2 static gains are the same
  Dominant pole=closes pole to y-axis=-2
  Dominant time-constant==-1/[Real(dominant pole)]=0.5
  at this time is the impulse response at (36%) or step response at

## Slide 17: Connecting blocks - book
Serial connection (cascading)
  Products of the elements
Parallel connection
  Sum of the elements
Feedback

## Slide 18: Connecting blocks – not in the book
X(s)
-
Y(s)
X(s)
Y(s)
X(s)
-
Y(s)
-
Y(s)
X(s)
-
Y(s)
X(s)
-
X(s)
Y(s)
Moving entry point backwards
Moving the exit point forwards
  Divide with the element moved over
Moving the entry point forwards
Moving the exit point backwards
  Multiple with the element moved over

## Slide 19: Example

## Slide 20: Step response 1

## Slide 21: Step response 2

## Slide 22: Exercise
http://homepages.vub.ac.be/~pcsurcsi/teaching.html
Typical mistakes
  Simulation time is too short and/or wrong scaling
Useful Matlab commands
  help,
  roots, tf, zpk, pzmap, cumsum,
  series, parallel, feedback,
  lsim, step, impulse, dcgain, stepinfo
  figure, plot, xlim, ylim, title, subplot, legend

## Slide 23: Bode plot - application

## Slide 24: Bode plot - application

## Slide 25: Bode plot - application
17.44 Hz
33.175 Hz
63.688 Hz
75.957 Hz
87.184 Hz
91.502 Hz

## Slide 26: P - Proportional term – 0 order tf

## Slide 27: I - Integral term
20 dB/D

## Slide 28: PI – Proportional Integral term
20 dB/D

## Slide 29: D – Derivative term
20 dB/D

## Slide 30: Dead time/ delay term

## Slide 31: T1 – 1st order term
20 dB/D
45 deg/D

## Slide 32: T1 – 1st order term
20 dB/D
45 deg/D

## Slide 33: PT1 – Proportional 1st order term
20 dB/D
45 deg/D

## Slide 34: T2 – 2nd order term as 2 T1 terms
20 dB/D
45 deg/D
40 dB/D
90 deg/D
45 deg/D

## Slide 35: T2 – 2nd order term, zeta=1
40 dB/D
90 deg/D

## Slide 36: T2 – 2nd order term, zeta=0.1

## Slide 37: T2 – 2nd order term, zeta=0.01

## Slide 38: Bode plot…
Static gain (0rad/sec)

## Slide 39: Control example
-3dB

## Slide 40: Control example in Matlab
clear all; close all;
s=tf('s');
H=1/(s-1);
subplot(131); impulse(H)
subplot(132); step(H)
subplot(133); bode(H); grid on
% PM=45 would be at w=1rad/sec; gain=-3.01 dB
K=sqrt(2); %3 dB moving up, 3dB is sqrt(2) in real numbers, 10^(3.01/20)
Hnew=K*H;
H_fb=feedback(Hnew,1);
subplot(131); impulse(H_fb)
subplot(132); step(H_fb)
subplot(133); bode(Hnew); grid on; hold on; bode(H)

## Slide 41: Analytical solution of the steady-state error
Final Value Theorem:
i.e. the time domain steady-state value equals the Fourier transform of the signal times s.
Calculate the open loop gain function
Write down the error:
  From here on:
  Which leads to
Replace R(s) wit the input signal, step input is
Apply 1: